| Type | Error Code | Reason | Action Item |
| --- | --- | --- | --- |
| Error | Startup failed. Please make sure your firewall is disabled. (error code: 10001) | Network is not stable and could not access P2P Server. | Check the network of the Client. |
|  |  | Web Client was blocked to access P2P server by firewall. | 1. Disable the Windows Firewall and try again 2. Disable the firewall of Router and try again. |
|  |  | P2P Server was down. | Fill ezNUUO Support Form and Contact with NUUO. |
| Error | Authentication failed. Please submit the technical inquiry at http://www.nuuo.com/eHelpdesk.php. (error code: 10002) | The authentication algorithm of P2P server might be changed. | Fill ezNUUO Support Form and Contact with NUUO. |
| Error | Connection failed. Please check the network of the NVR unit. (error code: 10003) | The Peer NVRSolo does not appear online, so P2P Server could not discovery it. | Check the network of the NVR unit (server). |
| Error | Tunnel connection failed. Please update the FW version of the NVR unit to the latest. (error code: 10004) | The P2P library might be out of date. P2P server could not make the P2P connection with the requested NVRSolo. | Update the FW version of the NVR unit to the latest. |
| Error | Connection stopped abnormally. Please make sure the network is stable and bandwidth is enough. (error code: 10005) | The network is not stable and bandwidth is not enough, which makes the connection stopped abnormally. | Check the network status on both server and client. |
| Error | Tunnel connection failed. Please submit the technical inquiry at http://www.nuuo.com/eHelpdesk.php. (error code: 10006) | Unknown reasons. | Fill ezNUUO Support Form and Contact with NUUO. |
| Error | Tunnel connection failed. Please submit the technical inquiry at http://www.nuuo.com/eHelpdesk.php. (error code: 10007) | Unknown reasons. | Fill ezNUUO Support Form and Contact with NUUO. |
| Warning | The server ID isn't existed. Please enter again. | The requested Server ID was not registered into ezNUUO database. | Make sure the server ID exists, and type again. |

# ezNUUO Support Form

| Item | Description |
| --- | --- |
| Issue |  |
| Error Code |  |
| Duplicate Ratio | % |
| Environment | Router 1 model name: Router 2 model name: |
| NVRsolo MAC Address 1 and Server ID | MAC Address 1 = Server ID = |
| TeamViewer ID on Client side | TeamViewer ID = Password = |